## Slide 1: Design Approach for Aerodynamics and Overall Impact
Jacob Keller
9/30/14

## Slide 2: Purpose
Develop design approach that estimates critical performance parameters that have been dictated by various requirements, such as, maximum weight, overall dimensions, available power, and ground roll.
  Provides a starting point from which aerodynamics (and others) can begin a detailed analysis (optimization).
  Big picture approach where the impact of design changes (estimates) can be investigated/examined.
Design approach compliments the conceptual design phase, where aerodynamics, propulsion, and performance are the major drivers.

## Slide 3: Design Approach
1. Requirements
2. First Weight Estimate
3. Critical Performance Parameters
a. Maximum Lift Coefficient
b. Lift-to-Drag Ratio
c. Wing Loading
d. Thrust-to-Weight Ratio
4. Configuration Layout (overall shape)
5. Better Weight Estimate
6. Performance Analysis
Does the design meet or exceed requirements?
7. Optimization – Achieve Best Design
Yes
No
Iterate

## Slide 4: 1. Requirements
Maximum Weight 55 lbs
L+W+H 175 inches
Ground Roll 200 feet
Maximum Power 1000 W

## Slide 5: 2. First Weight Estimate
Crude Estimate of GTOW:
Plot and vs or for past aircraft models to obtain reasonable estimate
  What is our goal for ?

## Slide 6: 3.1 Critical Performance Parameters: (
Initial Airfoil Shape: S1223
  Used on high lift model airplanes
  Will be optimized later, however, initially we will make an estimate for the maximum lift coefficient based on the unmodified S1223 airfoil
First Approximation of (:
  (
    is two-dimensional lift coefficient at the wing tip
    is two-dimensional lift coefficient at the wring root
    is change in maximum lift coefficient due to flap deflection
    is conversion from the two-dimensional lift coefficient to the three dimensional lift coefficient (between 0.9 and 1.0).
  Note: It is advantageous to have the airfoil thickness at the tip be smaller than at the root to encourage root stall before tip stall (aileron control). Additionally, washout should be investigated for the same purpose (.

## Slide 7: 3.2 Critical Performance Parameters:
Wing loading is usually determined by the stalling velocity, which we can approximate based on past aircraft models.
First Approximation for Wing Loading:
Plot vs wing loading or GTOW for past aircraft models
  Get an approximation for
Calculate the Planform Area, S:

## Slide 8: 3.3 Critical Performance Parameters:
Thrust-to-Weight Ratio determines the take-off distance, rate of climb, and maximum velocity. Since we are restricted by the take-off distance, we can approximate the required Thrust-to-Weight Ratio by:
  Note: This T/W is that at which the free-stream velocity is approximately equal to 0.7, as indicated in the equation above (thrust varies with velocity)
Note: There are some assumptions built into this equation, more specifically, that the T is much larger than D+. The next slide ignores this assumption.

## Slide 9: 3.3 Critical Performance Parameters: detailed
As mentioned on the previous slide, T/W determines the take-off distance, which the can be found with no assumptions by:
    is a proportionality constant associated with the increment in parasitic drag due to lift
    is the zero-lift drag coefficient ( is associated with extended landing gear: Assume
    is coefficient of rolling friction
    N = 1 for small aircraft (model aircraft) (Nis associated with ground covered during rotation phase, i.e., this may be neglected)
This forms a system of equations that can be solved for two important parameters, namely, the wing span and the T/W.
  Different Aspect Ratios will provide different values for T/W (assuming all other parameters are constant)
  This assumption may be valid for large aspect ratios (AR > 6), where the change in induced drag coefficient due to increasing AR may be considered negligible

## Slide 10: 3.3.1 Critical Performance Parameters: detailed
The zero-lift drag coefficient can be estimated in XFLR5, however, that requires a geometric shape, which we have not developed yet. Thus, the following equation provides an estimate for the zero-lift drag coefficient (this will probably be an iterative process since the power required to take-off is not yet known):
  where and can be approximated by:

## Slide 11: 4. Configuration Layout (Aerodynamics)
Wing:
  Geometric twist
  Taper ratio
  Variation in airfoil thickness
  High-wing, mid-wing, low-wing
Fuselage:
  Smooth changes in cross-sectional areas

## Slide 12: 4. Configuration Layout (General)
Stability and Control:
  Iterative process with aerodynamics group in determining if enough length is available for stability.
Structures:
  Are the suggestions by aerodynamics achievable (structurally safe, possible to build, etc.)?

## Slide 13: 5. Better Weight Estimate
Use all the above information to calculate the approximate GTOW (estimate weight of wings, motor, fuselage, landing gear, etc.)
Use all the above information to estimate the center of gravity

## Slide 14: 6. Performance Analysis
We’ve already insured two requirements were met, i.e., the maximum ground roll and L+W+H (dimensional limitations).
Next is determining if we have the power available to take-off, which is given by:
  where is:
  is a safety factor to ensure that 1000 Watts is never reached
If is too low or too high, adjustments can be made to the following parameters:
  Payload
  Wing loading

## Slide 15: 7. Optimization (Aerodynamics)
Optimize Aerodynamics Performance
  Wing, airfoil, and fuselage

## Slide 16: Aerodynamics Trade Study Sweep, Taper Ratios, and Fb
Andrew Clemens
9/30/14

## Slide 17: Purpose
Investigate effects of altering taper ratio, wing sweep, and the location where taper ratio begins.

## Slide 18
Taper Ratio Sweep
0.2  1.0 step size = 0.1
Outside peaks closest to center peak when taper ratio is 0.385
“Pinch” – due to change of rectangular to tapered

## Slide 19
Not recommended

## Slide 20
Taper Ratio Starting Location Sweep
0.2  0.8 step size = 0.1
Outside peaks closest to center peak when taper ratio is 0.385
Chart: CL Across Span (Fb Sweep)
Chart: CD Across Span (Fb Sweep)
Obtain balance between wingtip and root lift

## Slide 21
Taper Ratio Starting Location Sweep
Code accounts for TR in X, Y, & Z

## Slide 22
-15°, 0°, 15° Wing Sweep
Sweep does not affect Cl

## Slide 23
-15°, 0°, 15° Wing Sweep
Sweep does not affect Cd

## Slide 24: Airfoil Selection

## Slide 25: Airfoil Requirements
High lift (CL > 2)
Intended for low Reynolds numbers
  Competition Re ~405000

## Slide 26: Airfoil Comparison

## Slide 27: Attemped Reoptimization

## Slide 28: Polars for Aircraft Redesign